## Slide 1: ModalitY Review

## Slide 2: Type of Modality and Depth of Penetration
Electrical Stimulating Currents
    Depth of Penetration=
    Type of Modality=
Ultrasound
    Depth of Penetration=
    Type of Modality
Cryotherapy and Thermotherapy
    Depth of Penetration=
    Type of Modality=
Massage and Analgesics
    Depth of Penetration=
    Type of Modality=

## Slide 3: Depth of Penetration
Electrical Modalities
  Electrical Stimulating Currents
    Depth of Penetration= between the pads; very superficial
Acoustic Modalities
  Ultrasound
    Depth of Penetration= 3 to 5 cm
Infrared Modalities
  Cryotherapy (ice) and Thermotherapy (heat)
    Depth of Penetration= 1 cm
Mechanical/Manual Modalities
  Massage (deep tissue)-also a form of heat
    Depth of Penetration= based on pressure applied
  Analgesics (pain relieving cream/gel/ointment)

## Slide 4: Purpose of Cryotherapy
    Reduce ?
    Reduce ?
    Reduce ?
    4 Sensation Stages of Cryotherapy:

## Slide 5: Purpose of Cryotherapy
    Reduce blood flow (circulation)
    Reduce swelling and inflammation
    Reduce pain
    Sensation Stages of Cryotherapy:
    Cold, Pain, Burn/Sting, Numb

## Slide 6: Cryotherapy Options and Length of Treatment Time:
- Ice Bag- ?
- Cold Spray- ?
- Cold Whirlpool- (?°)
- Ice Massage/Ice Cup-?

## Slide 7: Cryotherapy Options and Length of Treatment Time:
- Ice Bag- 15 to 20 minutes
- Cold Spray- 10 to 15 seconds
- Cold Whirlpool- (50-55°) 8 to 10 minutes
- Ice Massage/Ice Cup- 5 to 8 minutes

## Slide 8: Contraindications for Cryotherapy
Do not use a cold treatment if the patient has the following situations:
  Allergy to cold
  Circulatory impairments
  Wound healing (open wounds/skin conditions)
  Hypertension- high blood pressure
  Skin anesthesia

## Slide 9: Purpose of Thermotherapy
  Increase ?
  Reduce ?
  Increase ?

## Slide 10: Purpose of Thermotherapy
  Increase blood flow (circulation)
  Reduce muscle stiffness
  Increase muscular relaxation

## Slide 11: Thermotherapy Options and Length of Treatment:
-Hydrocollator Pads-? minutes
-Hot Whirlpool (?˚)- ? minutes
-Massage- ? minutes

## Slide 12: Thermotherapy Options and Length of Treatment:
-Hydrocollator Pads-10 minutes
-Hot Whirlpool (?˚)- 8-10 minutes
-Massage- 8-10/30+ minutes

## Slide 13: Contraindications for Thermotherapy:
Do not use a heat treatment if the patient has the following situations:
  Acute and post acute trauma
  Poor circulation
  Malignancy (open wounds or skin conditions)
  Skin anesthesia

## Slide 14: Ultrasound
What type of modality is an Ultrasound?
What is the depth of penetration?
Why do we use ultrasound as a therapeutic treatment?

## Slide 15: Ultrasound
Ultrasound is defined as inaudible, acoustic vibrations of high frequency that may produce either thermal or non thermal physiological effects.
This modality stimulates repair of soft tissue and pain relief.
It is a form of acoustic energy used for deep tissue heating.
  Depth of penetration= 3 to 5 cm

## Slide 17: What is the Frequency and Intensity for Ultrasound?
  Frequency range between _____ and _____ MHz
    ______ MHz ultrasound allows for deeper penetration while _____ MHz is absorbed more superficially
  Area of transducer that produces sound is the effective radiating area
  Intensity is measured or delivered in (W/cm2).
    Non-thermal Ultrasound= ___________

## Slide 18: What is the Frequency and Intensity for Ultrasound?
  Frequency range between .75 and 3.0 MHz
    1 MHz ultrasound allows for deeper penetration while 3 MHz is absorbed more superficially
  Area of transducer that produces sound is the effective radiating area
  Intensity is determined by amount of energy delivered to the sound head (W/cm2)
    Non-thermal Ultrasound= under .2 W/cm2

## Slide 19: Ultrasound Application to the Skin
What are the 3 methods or techniques to use the Ultrasound?

## Slide 20: Ways to Apply the Ultrasound Machine to the Skin.
Application
  Direct skin application
  Underwater application
    Used for irregularly shaped structures
    Body part is submerged in water
  Bladder technique
    Used when body part can not be immersed in water
    Balloon filled w/ gel or water

## Slide 21: How fast do you move the Ultrasound?
  Moving the transducer
    Should be moved at a rate of _______ cm/sec
    Must maintain contact of transducer with surface of skin
    Circular or stroking patterns should be used

## Slide 22: How fast do you move the Ultrasound?
  Moving the transducer
    Should be moved at a rate of 4cm/second
    Must maintain contact of transducer with surface of skin
    Circular or stroking patterns should be used

## Slide 23: Treatment Time and Contraindications
  Time
    Duration tends to last ________ minutes
  Contraindications
    ???

## Slide 24: Treatment Time and Contraindications
  Time
    Duration tends to last 5-10 minutes
  Contraindications
    Be careful with anesthetized areas, reduced circulation
    Avoid high fluid regions of the body, acute injuries, and epiphyseal areas of children

## Slide 25: Electrical Muscle Stimulator
  _____________________ is applied to nerve tissue at certain intensities and duration to reach tissue excitability thresholds resulting in membrane depolarization

## Slide 26: Electrical Muscle Stimulator
  Electricity is applied to nerve tissue at certain intensities and duration to reach tissue excitability thresholds resulting in membrane depolarization
    Target sensory, motor, and pain nerve fibers in an effort to produce specific physiological effects

## Slide 28: Types of E-stim and its Purpose
Electrical Stimulating Units
  Three types of units
  Purpose for using E-stim

## Slide 29: Types of E-stim and Purpose
Electrical Stimulating Units
  Three types of units
    TENS - transcutaneous electrical nerve stimulators
    NMES/EMS - neuromuscular electrical stimulators or electrical muscle stimulators
    MENS/LIS – micro-current electrical nerve stimulators or low-intensity stimulators
  Purpose for using E-stim
      Useful in pain modulation and muscle contractions

## Slide 30: Ultrasound Indications and Treatment TIme
Indications
Treatment Time = __________ minutes

## Slide 31: Ultrasound Indications and Treatment Times
Indications
  Pain Modulation- 80 pps
  Muscle Contraction-20-60 pps
    Muscle pump
    Muscle strengthening
    Retardation of atrophy
    Muscle re-education
    Treatment time 15-20 minutes and repeated multiple times over the course of a week

## Slide 32: Why Massage???

## Slide 33: Why Massage???
  Encourage lymph drainage
  Stretch superficial scar tissue
  Stretch connective tissue (friction massage)
  Increase circulation – due to increased metabolism
  Relaxation

## Slide 34: Massage Strokes- What technique is used First?

## Slide 35: Massage Strokes- What technique is used First?
Effleurage
  Stroking divided into light and deep

## Slide 36: Effleurage

## Slide 37: What massage technique involves Kneading?

## Slide 38: What massage technique involves Kneading?
Petrissage
  Involves picking up skin between thumb and forefinger, rolling and twisting in opposite directions

## Slide 39: What type of Massage Technique is this?

## Slide 40
  Tapotement
    Cupping
    Hacking
    Pinching

## Slide 41: Guidelines for Massage
  Make the athlete comfortable
  Develop confident, gentle approach to massage
  Stroke towards heart to enhance lymphatic and venous drainage
  Know when to avoid massage
    Acute conditions and skin conditions